## Slide 1: REMOTE SENSING BASICS George Senyo Owusu georgeowusu@ug.edu.gh Center for Remote Sensing and Geographic Information Services (CERSGIS)
Accra, Ghana
September, 2021

## Slide 2
REMOTE SENSING:
  The art and science of obtaining information about an object without physically contact between the object and sensor
  The processes of collecting information about Earth surfaces and phenomena using sensors not in physical contact with the surfaces and phenomena of interest.
  There is a medium of transmission involved i.e. Earth’s Atmosphere.
Some Remote Sensors

## Slide 3
Some Remote Sensors

## Slide 4: History of Remote Sensing
Balloon photography (1858)
Pigeon cameras (1903)
Kite photography (1890)
Aircraft (WWI and WWII)
Space (1947)
Images: Jensen (2000)

## Slide 5: Remote sensing cycle
Remote Sensing Includes:
  A) The mission plan and choice of sensors
  B) The reception, recording, and processing of the signal data
  C) The analysis of the resultant data.

## Slide 6
Energy Source or Illumination (A)
Radiation and the Atmosphere (B)
Interaction with the Target (C)
Recording of Energy by the Sensor (D)
Transmission, Reception, and Processing (E)
Interpretation and Analysis (F)
Application (G)
Source: Canadian Centre for Remote Sensing
Remote Sensing Process Components

## Slide 7: Electromagnetic Spectrum

## Slide 8: Electromagnetic Radiation

## Slide 9: Signature Spectra

## Slide 10: Fundamental term
All remote sensing systems have four types of resolution:
  Spatial
  Spectral
  Temporal
  Radiometric
Resolution

## Slide 11: Spatial Resolution
The earth surface area covered by a pixel of an image is known as spatial resolution
Large area covered by a pixel means low spatial resolution and vice versa
High vs. Low?
Source: Jensen (2000)

## Slide 12: Spectral Resolution
Is the ability to resolve spectral features and bands into their separate components
More number of bands in a specified bandwidth means higher spectral resolution and vice versa

## Slide 13: Spectral Resolution

## Slide 14: Three spectra recorded at low, medium and high spectral resolution, illustrating how the high resolution mode yields sharper peaks, and separates close lying peaks, which are merged together at low resolution
Spectral Resolution

## Slide 15: Temporal Resolution
Frequency at which images are recorded/ captured in a specific place on the earth.
The more frequently it is captured, the better or finer the temporal resolution is said to be
For example, a sensor that captures an image of an agriculture land twice a day has better temporal resolution than a sensor that only captures that same image once a week.

## Slide 16: Radiometric Resolution
Sensitivity of the sensor to the magnitude of the received electromagnetic energy determines the radiometric resolution
Finer the radiometric resolution of a sensor, if it is more sensitive in detecting small differences in reflected or emitted energy

## Slide 17
Radiometric Resolution
1023
6-bit range
0
63
8-bit range
0
255
0
10-bit range
2-bit range
0
4

## Slide 18: Types of Remote Sensing
Aerial Photography
Multispectral
UAVs and Drones
Active and Passive Microwave and LIDAR

## Slide 19: Some known satellites
NOAA-AVHRR (1100 m)
GOES (700 m)
MODIS (250, 500, 1000 m)
Landsat TM and ETM (30 – 60 m)
SPOT (10 – 20 m)
IKONOS (4, 1 m)
Quickbird (0.6 m)

## Slide 20: Applications of Remote Sensing
Urban & Regional Planning
Mapping & updation of city/town maps
Urban sprawl monitoring
Town planning
Facility management
GIS database development
Scope
Lyari Express Way – Section (Essa Nagri)
Better decision support, planning & management
Rapid information updation
Infrastructure development monitoring
Spatial information analysis
Benefits

## Slide 21
Agriculture
Crop acreage estimation
Crop modeling for yield & production forecast / estimation
Crop & Orchard monitoring
Scope
Timely availability of crop statistics for decision making & planning
Crop growth monitoring
Soil status monitoring
Regular reports regarding total area under cultivation
Benefits
Banana Plantation – Muhammad Pur (Ghotki)
FFC Goth Macchi
Mar 05, 2006, Recovery
Jan 12, 2006, Damage
Dec 16, 2005, Pre-Frost

## Slide 22: Flood Damage to Standing Crops
Pre Flood – 17 July 2006
Post Flood – 09 Aug 2006
10098 acr
3516 acr
● Phulani
● Goth Lataran
● Ural
● Junno Dhand
● Shahpur
● Godhpur
● Than Lake
● Goth Azizpur
● Goth Raza Mahar
● Phulani
● Goth Lataran
● Ural
● Junno Dhand
● Shahpur
● Godhpur
● Than Lake
● Goth Azizpur
● Goth Raza Mahar
● Muhro Mari
● Darapur
● Kot Shahgarch
● Muhro Mari
● Darapur
● Kot Shahgarch

## Slide 23
Forestry
Satellite image based forest resource mapping and updation
Forest change detection
Forest resource inventory
GIS database development
Scope
Availability of baseline information
Planning for aforestation strategies
Futuristic resource planning
Sustainability of environment
Wild life conservation & development for recreation purpose
Benefits
Sarhad Reserve Forest (Ghotki)
Nausharo
Firoz

## Slide 24
Coast Resource Mapping
Satellite image
Mangroves forest map
Mangrove forest monitoring
Change detection
Hazard impacts
Aqua-culture zones
Scope
Benefits
Availability of updated information on mangroves forest
Planning strategies for aforestation and deforestation trend
Timely Intervention in specific areas as and when needed

## Slide 25
Landuse / Landcover Mapping
Monitoring dynamic changes
Urban/Rural infrastructure
Waterlogging & salinity
Scope
Assessment of spatial distribution of land resources
Infrastructure monitoring
Availability of usable land
Future planning for better land management for socio-economic development
Benefits